## Slide 1
A watershed approach to managing rainfed agriculture in the semi-arid region of southern Mali: Integrated research on water and land use
Africa RISING West Africa Phase 1 Review and Legacy Workshop
December 12-13, 2016, Samanko-Bamako, Mali
Birhanu Z. Birhanu, Kalifa Traore, Murali K. Gumma, Ramadjita Tabo and Anthony Whitbread

## Slide 2
Outline
Introduction and Objectives
Research Approach
Main Results and Discussion
Conclusions

## Slide 3
West Africa Sahel is characterized by low, irregular rainfall pattern with high PET, and low potential for surface runoff storage.
  Measures that could improve moisture availability in the sub surface are required.
  Activities need to ensure that:
    wells are recharged
    soil moisture and farm nutrients are maintained
    erosion and runoff are minimized
  Establishing and characterization of watershed areas for integration of research activities
  Evaluation of appropriate SWC technologies
Introduction and Objectives

## Slide 4
Target group
Breeders
Social scientists
Hydrologists
System modelers
Planners
Crop type / intensity
Tracking adoption of NRM technologies
Abiotic stresses
Mali
Land use / land cover
Impact assessment
Watershed
prioritization
Biomass (g/m2)
LGP / planting dates
Biomass

## Slide 5
Chart: Percentage of Structure
| Shallow Well | CBT | Vegetative Barrier | Bund (stone or soil) | Contour Farming | Deep Tillage | Constructed water pool | Dam or dike | other
% of Structure | 32 | 26 | 12 | 12 | 6 | 6 | 3 | 2 | 1
Water and soil fertility management structures
Source of water for household water demand

## Slide 6
Chart: Percentage of Response (%)
| Conservation of soil and water | Prevention of gulley formation | Conservation of soil fertility
Very High | 33 | 31 | 42
High | 48 | 41 | 43
Medium | 17 | 20 | 15
Low | 2 | 8
Specific efficiency of land and water management structures (perception of farmers)
Chart: Percentage of Responses
| Water Availability | Yield | Fertility
 | 0.46154 | 0.38462 | 0.15385
Details concerning success stories (perception of farmers)
Further Reading: Birhanu et al.,2014, RDS Research Report No 63
SWC measure | Male headed (n=244) | Female headed (n=37) | T- statistic | P-value
Zai | 0.43 (0.50) | 0.35 (0.48) | -0.95 | 0.34
Artificial ponds | 0.23 (0.42) | 0.24 (0.43) | 0.24 | 0.81
Vegetative barriers | 0.23 (0.42) | 0.27 (0.45) | 0.54 | 0.54
Courbes de niveau (ridges) | 0.23 (0.42) | 0.24 (0.43) | 0.18 | 0.18
Shallow Wells | 0.23 (0.42) | 0.24 (0.43) | 1.08 | 0.28
Irrigated fields | 0.22 (0.41) | 0.30 (0.46) | -1.46 | 0.15

## Slide 7: Research Approach
  Identification of a site for small scale intervention work
  Monitoring and Modeling: Installation of hydro-meteorological monitoring stations and participatory monitoring at watershed scale
  Technological improvement and experimental study on SWC technologies
  Evaluation of the land use dynamics over period of time

## Slide 8: Data used
Survey data on land and water management practices
Daily climate data from nearby station (1980 to 2010)
Newly instrumented sites
Soil sampling and profiling
Shallow wells
CGIAR SRTM data
Field experimentation of soil and water management practices

## Slide 9: Study site

## Slide 10: Watershed management program benefiting farmers in Mali
Moving from traditional water access to improved technology through use of Technology Parks and Innovation Platforms
Improved land management practices, contour bunding and agro forestry options

## Slide 11
Chart: Year
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010
Annual Rainfall | 755.4 | 849.6 | 849.3 | 794.6 | 516.3 | 774.7 | 897.8 | 704.3 | 901.5 | 667.2 | 1057.7 | 862.1 | 729.1 | 728.2 | 1358.4 | 837.6 | 779.9 | 1009.1 | 1036.1 | 864.3 | 738.3 | 776.8 | 627 | 905.3 | 667 | 771.7 | 996.9 | 963.4 | 722.6 | 919.7 | 1137.2
259 Shallow wells investigated
Chart: Year of construction
10 wells
114 wells
130 wells
Chart: Depth of Shallow Well (m)
| [3.5-8.5] | [8.5-13.5] | [13.5-18.5] | [18.5-23.5] | [23.5-28.5] | [28.5-33.5]
Frequency (%) | 0.15574 | 0.31967 | 0.38934 | 0.065574 | 0.057377 | 0.012295
p-value 0.032
Chart: Depth of water in shallow well in dry season (m)
| [3.5-6.5] | [6.5-9.5] | [9.5-12.5] | [12.5-15.5] | [15.5-18.5]
Quantitative data - Depth of the water in the dry season | 0.30303 | 0.36364 | 0.18182 | 0.12121 | 0.030303
p-value 0.996
Chart: Depth of water in shallow well rainy season (m)
| [0-4] | [4-8] | [8-12] | [12-16] | [16-20]
Fréquence | 0.52 | 0.24 | 0.04 | 0.12 | 0.08
p-value 0.707
Further Reading
Birhanu and Tabo 2016
J.Ag &Food Security

## Slide 12
Rainfall recording
Soil moisture recording
Automatic Weather Station
Monitoring shallow well

## Slide 13
Monitoring surface runoff & erosion

## Slide 14: Installation of water table measurement tubes

## Slide 15
Soil sampling and profiling

## Slide 16
  Satellite imagery & analysis for LULC mapping
Total Ag area in ha:
1618 (1991),
2197 (2002)
2498 (2014)
LULC# | Sep-91 |  | Sep-02 |  | Sep-14 | 
 | Area (ha) | % | Area (ha) | % | Area (ha) | %
01.Rainfed-SC-cotton/maize | 390 | 7% | 782 | 14% | 1621 | 28%
02. Rainfed-SC-sorghum | 1247 | 22% | 1415 | 24% | 1061 | 18%
03.Rainfed-SC- Sorghum/Trees mix | 0 | 0% | 1009 | 17% | 822 | 14%
04.Rangelands/Shrublands | 4108 | 71% | 2531 | 44% | 2245 | 39%
05. Water bodies | 0 | 0% | 7 | 0% | 2 | 0%
06. Built-up lands | 34 | 1% | 35 | 1% | 29 | 1%

## Slide 17
Chart: Date
| 42184 | 42191 | 42193 | 42195 | 42197 | 42200 | 42203 | 42205 | 42207 | 42210 | 42211 | 42213 | 42216 | 42218 | 42223 | 42226 | 42227 | 42229 | 42230 | 42234 | 42236 | 42237 | 42241 | 42243 | 42245 | 42248 | 42255 | 42262 | 42264 | 42266 | 42267 | 42268 | 42274 | 42276
Treatment | 2.4603 | 30.1587 | 8.7302 | 20.6349 | 7.619 | 6.3492 | 8.3333 | 0.47619 | 0.79365 | 7.5397 | 0.35714 | 11.9048 | 6.1111 | 4.3651 | 0 | 23.0159 | 0.47619 | 6.1905 | 1.6667 | 9.3651 | 7.5397 | 7.7778 | 6.1905 | 9.5238 | 5.9524 | 6.9048 | 1.5079 | 0.15873 | 7.3016 | 3.8889 | 0.47619 | 0.87302 | 8.3333 | 3.6508
Control | 5.4762 | 39.6825 | 12.2222 | 30.1587 | 14.127 | 15.0794 | 13.4921 | 2.3016 | 2.7778 | 11.9048 | 1.5873 | 15.4762 | 12.381 | 9.127 | 0.39683 | 29.7619 | 0.59524 | 11.9841 | 5.7937 | 15.4762 | 11.9048 | 13.1746 | 11.5079 | 15.6349 | 12.8571 | 15.7937 | 2.7778 | 0.43651 | 9.6825 | 9.127 | 1.1905 | 2.1429 | 16.9841 | 10
Rainfall | 14.5 | 91 | 24.5 | 52 | 25 | 35 | 30 | 9 | 9 | 22.5 | 4.75 | 30.5 | 23 | 19 | 8 | 73 | 4.75 | 20.5 | 12.5 | 38.5 | 22.5 | 29 | 27.5 | 34.5 | 24.5 | 35 | 7 | 5.5 | 29 | 16.5 | 7.5 | 9.5 | 35 | 20
n = 34
P-value = 0.018
Chart: Runoff coefficient
| Sekou Berthé | Madou Berthé | Mean
Treatment | 26.0817 | 24.4901 | 25.2859
Control | 39.7149 | 43.4495 | 41.5822
Variation in runoff rate
39 to 43% (Control)
24 to 26% (Treatment)
In-field SWC experimentation: Evaluating Sedimentation and Runoff

## Slide 18
July (beginning of the rainy season)
August-September (mid rainy season)
October-November (end of the rain)
Maximum SM (27%) was observed in the first 40 cm soil layers after which water content decrease and is similar until 80 cm depth (22%) and finally reach about 21% for the treatment plot and 13% for the non treated plot at 100 cm depth.
Maximum SM (35%) in treated field was observed until 80 cm depth. The mid season was characterized by presence of frequent rainfall and deep drainage.
End of the rainy season, drainage was deep with less water (about 20 % at 60 cm).
Soil moisture was at least 25% explaining possible water supply for trees.
Soil Moisture (SM) was always greater in treatment field.
In-field Soil and Water conservation experimentation: Evaluating Soil Moisture Dynamics

## Slide 19: Conclusions and recommendations
Established technology parks and innovation platforms in identified watershed sites provided a new dimension to evaluate and demonstrate new technologies, provide hands-on training to farmers and students, and determined farmers’ preferences for technologies-an important input for scaling approach
Insignificant variation in water level depths in different seasons. This goes to show that water is available at a depth that could be accessed easily should there be an appropriate water lifting mechanisms.

## Slide 20
Significant reduction in runoff rate and increased soil moisture presence in the sub surface when fields were treated with SWC practices.
Historical LULC study showed that increasing cropland area was at the expense of natural vegetation. There were not many studies that evaluated the changes in productivity over time and the damage caused to the natural resources (i.e. land degradation). Further research is recommended here.

## Slide 21
Watershed research is a long term collective effort. To be effective strong institutional support is required at all levels.
  Presently there is a big interest from the national agricultural research institution (IER) and local NGO AMEDD in Mali for watershed program.
  IER in applied and adaptive research & AMEDD for their connection, via the extension service, to local communities and farmers makes IER and AMEDD potentially very important actors in the watershed development program in Mali.

## Slide 22
Merci